Table X1: Egrett payload

| Instrument | Measurement | PI |
| --- | --- | --- |
| Basic Meteorology and position | Pressure, temperature, wind, GPS (1 Hz) | Jorg Hacker, Airborne Research Australia |
| DMT Single Particle Soot Photometer (SP-2) † | Aerosol particle size distribution (0.2 – 1.0 µm), light-absorbing fraction and composition | Hugh Coe, Univ. Manchester, UK |
| 2 x TSI-3010 Condensation Particle Counter (CPC) | Total condensation particles > 10 nm & > 80 nm | Martin Gallagher, Univ. Manchester, UK |
| DMT Cloud, Aerosol & Precipitation Spectrometer (CAPS) | Cloud droplet spectrum, aerosol/small particle asymmetry, aerosol refractive index, (diameter 0.3- 2000 µm) | Andy Heymsfield, NCAR, Boulder, USA |
| DMT Cloud Droplet Probe (CDP) | Cloud Particle Size Distribution (diameter 2 - 60 µm) | Martin Gallagher, Univ. Manchester, UK |
| SPEC Cloud Particle Imager CPI-230 | Cloud particle/ice CCD images, (diameter 30 - 2,300 µm) | Martin Gallagher, Univ. Manchester, UK |
| Buck Research CR-2 frost point hygrometer | Ice point temperature, 20 s, ( 0.1( | Reinhold Busen, DLR, Germany |
| Open path tuneable diode laser hygrometer | Water vapour concentration, 1s, (1 ppmv | Jim Whiteway, York Univ., Canada |
| Closed path tuneable diode laser hygrometer | Water vapour concentration, 1s, (1 ppmv | Geraint Vaughan, Univ. Manchester, UK |
| CO analyser | Carbon monoxide, 1 Hz, ± 2 ppbv | Andreas Volz-Thomas, FZ Jülich, Germany |
| Miniature Gas-Chromatograph | Halocarbons (Cl, Br, I), 3-6 min, ( 5% | Neil Harris, Univ. Cambridge, UK |
| TE-49C UV Ozone sensor | Ozone concentration (± 2 ppbv, 10 seconds) | Reinhold Busen, DLR, Germany |
| Automatic Tube Sampler (ATS), 15 per flight | C4-C9 aliphatics, acetone, monoterpenes, OVOCs | Alastair Lewis, York Univ., UK |
| NO and NO2 chemiluminescent detector † | ( 200 ppt @ 10 Hz; ( 30 ppt @ 4 s integration | Andreas Volz-Thomas, FZ Jülich, Germany |

† alternates (only one flown at any time)

Table X2: Dornier payload

| Instrument | Measurement | PI |
| --- | --- | --- |
| Aventech AIMMS-20 probe | GPS position, pressure, temperature, relative humidity, winds, 1 Hz | David Davies, ARSF |
| Aerosol Mass Spectrometer | Aerosol size and composition, 30 – 2000† nm | Hugh Coe, Univ. Manchester, UK |
| TSI3010 Condensation particle counter | Aerosol concentration > 10 nm, 1 Hz | Martin Gallagher, Univ. Manchester, UK |
| Grimm Optical Particle Counter | Aerosol size distribution, 0.3 – 2† μm, bins 0.1 – 0.2 μm, 0.16 Hz | Martin Gallagher, Univ. Manchester, UK |
| Ultra high sensitivity aerosol spectrometer | Aerosol size distribution 0.3 – 0.8 µm, 7.5 nm bins, 1 Hz. | Martin Gallagher, Univ. Manchester, UK |
| Aerosol spectrometer probe | Aerosol size distribution, 0.2 – 2† µm, bins 0.03 – 0.5 µm, 0.1 Hz | Martin Gallagher, Univ. Manchester, UK |
| Forward scattering spectrometer probe (FSSP) | Aerosol and cloud droplet size distribution, 0.5 - 32 µm, bin 0.8 µm, 0.1 Hz | Martin Gallagher, Univ. Manchester, UK |
| Particle soot absorption spectrometer (PSAP) | Black carbon concentration (aerosol), ± 1 μg m-3, 0.2 Hz | Andreas Minnikin, DLR, Germany |
| Filters | Coarse aerosol composition, whole flight accumulation | Keith Bower, Univ. Manchester, UK |
| 2B technologies model 202 ozone monitor | Ozone concentration, ±2 ppbv, 0.1 Hz | Alastair Lewis, York Univ., UK |
| Aerolaser AL5003 | Carbon monoxide concentration, ± 1 ppbv, 1 Hz | Alastair Lewis, York Univ., UK |
| Automatic Tube Sampler (ATS), 15 per flight | C4-C9 aliphatics, acetone, monoterpenes, OVOCs | Alastair Lewis, York Univ., UK |
| Chemiluminescence/catalysis | NO/NOx/NOy | James Lee, York Univ., UK |
| Miniature Gas-Chromatograph | Halocarbons (Cl, Br, I), 3-6 min, ( 5% | Neil Harris, Univ. Cambridge, UK |

† Upper bound limited by inlet efficiency