## Slide 1: Progress in Neuromorphic Photonics
Thomas Ferreira de Lima*, Bhavin J. Shastri, Alexander N. Tait, Mitchell A. Nahmias and Paul R. Prucnal
Lightwave Communications Research Laboratory, Department of Electrical Engineering, Princeton University, Princeton, NJ 08544, USA.
Corresponder e-mail: tlima@princeton.edu
Mark Kynigos

## Slide 2: But… Why?
Why neuromorphic?
  Bio-inspired energy efficient specialized co-processors
  Estimated human brain computation efficiency: MAC/s with 20W of power
Limitations in electronics:
  Large amount of interconnects (IC)/ multicasting introduces physical performance challenges
  Operations per neuron in the kHz- low MHz regime
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 3: But… Why?
Mark Kynigos
Why photonics?
  Significantly increased bandwidth density of ICs
  Potentially very energy efficient
  Relatively distance-independent energy consumption compared to electronics
Limitations:
  Requires nascent manufacturing technology (SiPh platforms)
  Prone to noise and optical losses
Progress in Neuromorphic Photonics

## Slide 4: But… Why?
Mark Kynigos
Why neuromorphic photonics?
  Best of both worlds:
    energy efficiency through computation model & interconnect
    More computational speed through photonic IC for specialised domains ( e.g. Real-time RF processing, QP)
  Hybrid SiPh manufacturing platforms
    passive & active optical component integration on-chip
Progress in Neuromorphic Photonics

## Slide 5: Key Criteria for Nonlinear Elements
Enabling scalable platforms:
  Thresholding
  Max. fan-in
  Cascadability
“Neuromorphism”:
  Isomorphism between artificial NNs and optoelectronic devices
  Nonlinearity in individual neurons
  Synaptic interconnection
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 6: Basic Requirements for Photonic Neurons
Basic operations:
  Vector Multiplication
  Spatial summation
  Non-linear transformation
Hardware provision:
  Signal integrity
  Scalable max. fan-in
  Enough output power to drive the neighbours (cascadability)
Mark Kynigos
WDM compatibility?
Progress in Neuromorphic Photonics

## Slide 7: Photonic Network Node (PNN)
A networkable photonic device with optical I/O that can emulate an artificial neuron
PNN types:
  All-optical (Fig. 3A, 3B): Based on excitable lasers
  Optical-electrical-optical (O/E/O) (Fig. 3C)
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 8: All-optical PNNs: Excitable Lasers
Excitable system criteria:
  there is only one stable state at which the system can indefinitely stay at rest
  when excited above a certain threshold, the system undergoes a stereotypical excursion, emitting a “spike”
  after the excursion, the system decays back to rest in the course of a “refractory period” during which it is temporarily less likely to emit another spike
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 9: All-optical PNNs: Excitable Graphene Laser
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 10: All-optical PNNs: LIF Analogy
Mark Kynigos
Progress in Neuromorphic Photonics
Near-threshold laser dynamics:
LIF Model:
If , then release a spike and set →, where is the membrane voltage, is the membrane resistance, is the equilibrium potential, and is the applied current (input).
If , then release a pulse and set →, where models the gain, is the gain carrier relaxation rate, is the gain bias current. is the input for spike firing times , is the gain threshold and is the gain at transparency.

## Slide 11: All-optical PNNs: Excitable Laser Circuits
Mark Kynigos
Progress in Neuromorphic Photonics
Cascadability
Temporal Pattern Recognition

## Slide 12: O/E/O PNNs: Breakdown
E/O sub-circuit: non-linear component
  Electronic input (weighted sum of optical inputs)
  Perform dynamic or nonlinear process
  Generate a clean optical output on a single wavelength
O/E sub-circuit: weighted addition
  Protocol?
  Hardware?
  Use WDM for scalability?
Mark Kynigos
Progress in Neuromorphic Photonics
O/E WDM weighted addition
E/O non-linearity

## Slide 13: O/E/O PNNs: E/O Nonlinearity Generation
Mark Kynigos
Progress in Neuromorphic Photonics
Most promise, nascent tech.
Ultrafast modulator not demonstrated
Off-chip lasers well understood, less energy efficiency and coupling probs.
Need to operate slow enough for output digitization
On-chip lasers generate energy savings but contribute to power env.
Same as C

## Slide 14: PNN Network Architecture: O/E Component
Protocol: Broadcast-and-weight
  Similar to fibre telecom “Broadcast and Select”
  WDM input fed to MRR weight bank which performs weighted add
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 15: PNN Network Architecture: Weight bank limits
Weight bank controllers limited by thermal crosstalk handling
  Each wavelength corresponds to a heating level at the MRR tuner heat affects neighbours
  Non-ideal fabrication-isolation reduces the weight range
Mark Kynigos
Progress in Neuromorphic Photonics
Channel limits:
  Depending on MRR type, between 108-334 channels
  Limits connectivity scaling (max. fan-in)

## Slide 16: Scaling solutions:
Spectrum reuse strategies
Exploiting interference in MRR weight banks
More degrees of freedom in multiplexing (mode division, polarization division)
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 17: Scaling solutions: Spectrum reuse
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 18: Neuromorphic Platform Comparison
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 19: Neuromorphic Photonic proc. Applications (1)
Real-time RF processing, massive MIMO systems
Most radio transceiver systems are processed by DSPs or FPGAs
  Carrier signal throughput (GHz range) is limited by processor speeds
  Sampling-parallelisation helps at the cost of more latency/energy overhead
  ASICs are expensive/not reconfigurable
Use Neuromorphic Photonic hardware for dimensionality reduction tasks (PCA, blind-source separation)
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 20: Neuromorphic Photonic proc. Applications (2)
Nonlinear programming, QP
Model predictive control problem can be reduced to a QP problem
  MPC is successfully used in “slow” processes, i.e. sufficient time for solving the optimization problem between sampling instants.
  Applying MPC to faster systems requires faster QP solving
  QP can be mapped onto recurrent neural networks
Neuromorphic Photonic hardware offers low ToF for communication, which somehow means less latency.
Mark Kynigos
Progress in Neuromorphic Photonics

## Slide 21: Paper Critique
Written for photonics engineers
Very focused on thermally tuned MRRs for weight banks, no talk of other devices (e.g. AWGRs, E/O MRRs)
Not enough focus on comm. protocols, WDM schemes
Seems like a lot of assumptions for platform comparison
Mark Kynigos
Progress in Neuromorphic Photonics
Pros
Cons
Good overview of current research efforts
Well written, good narrative, digestible
Nice trade-off analysis for photonic weight banks
Application section

## Slide 22: Supplementary: 3D Integrated Nanophotonic Neuromorphic Computing @ UC Davis
Mark Kynigos
Progress in Neuromorphic Photonics
Info at:
https://sierra.ece.ucdavis.edu/index.php/2020/03/21/neuromorphic-computing-with-3d-integrated-nanophotonic-neurons/
https://sc17.supercomputing.org/SC17%20Archive/tech_poster/poster_files/post272s2-file2.pdf

## Slide 23: Thank you!
Progress in Neuromorphic Photonics